## Slide 1: From zero to PCB hero
A small intro to KiCad

## Slide 2: The plan for today
Get KiCad installed
Baby's first KiCad project
Exporting for manufacture
Organizing large projects
Best practice, cheatsheets and all that good stuff

## Slide 3: The important questions
Where is it?
What is it?
Why should we use it?

## Slide 4: Where is KiCad?
https://www.kicad.org/download/

## Slide 5: What is KiCad?
Schematic design
PCB design
Bill of materials
Simulation
Much much more

## Slide 6: Why is KiCad?
No license needed
Open source
Runs on every operating system
It's Free!

## Slide 7: The design flow in broad terms
Schematic
Pcb layout
(Crying because you forgot footprints)
More Pcb layout
Ordering / Routing yourself
Finished physical pcb

## Slide 8: Setting up a new KiCad project
Empty project
From template
Clone from Repository

## Slide 9: Schematic setup

## Slide 10: PCB setup
Board layers
Routing constraints
Track and via sizes
Net classes
And much more...

## Slide 11: Simple buck converter with LM2575
A small starter project

## Slide 12: Only 5 components 
https://www.komponenten.es.aau.dk/fileadmin/komponenten/Data_Sheet/Spaendingsreg/LM2575.pdf

## Slide 13: Let us go into KiCad
But first, a 3.14 minute break

## Slide 14: Inserting a symbol
Press A
Search for the symbol/part you want to insert
Remember to select a footprint

## Slide 15: Schematic editor shortcuts
A – place component
W – draw connection
P – place power label
L – place local label
Ctrl+L – place global label

## Slide 16: Pcb editor shortcuts
V – Switch between top/bottom layer
F – move selected to other layer
X – Route single track
U – select whole track
B – Recalculate all filled zones

## Slide 17: Exporting your board for production
In-house fabrication
Ordering

## Slide 18: In-house

## Slide 19: Ordering
Same procedure, but more options can be exported
Check exported files using JLCDFM before ordering
https://jlcdfm.com/

## Slide 20: Kicad Cheatsheet
https://forum.kicad.info/t/kicad-v8-cheatsheet/51774

## Slide 21: PCB design pitfalls
Always use as wide a trace as possible
  0.4 mm / 0.6mm is ideal for traces
Every component/IC/Transistor/Regulator should be decoupled using a 1-100n capacitor
  Except some rare cases
The goal is to get the shortest path for every trace from A to B
Good PCB-design Requires a certain level of OCD
Proper PCBs
Our homemade PCBs

## Slide 22: Examples – what not to do
A project doomed from the start
”You already paid for all the copper so you
might as well use it” – Axel Olsson

## Slide 23: Examples – what not to do
Other things
Avoid Highspeed
  If you have a problem
High currents?
  Your traces are resistors (and fuses as well)
  Outer layer:
Looks pretty good
O_o
So thin?
A garden pump controller
Designed by yours truely (It never worked that well)
No decoupling!?

## Slide 24: BREAK TIME

## Slide 25: Power and Ground stackup
Life is short, use 4 layer for ”real” pcb’s

## Slide 26
Source: https://resources.altium.com/p/4-layer-pcb-stackup

## Slide 27: Organizing larger projects
Building on Ben’s lovely PCB course
  Hierchal sheets
Pin management
Vector/Group Busses

## Slide 28: Hierarchical design
Splitting the board into functionalities
STM32H7B0VBT

## Slide 29: Hierarchical design – interfaces
The pin connectors
Source: https://docs.kicad.org/master/en/eeschema/eeschema.html
Local labels
Global labels
Hierachal label
This one is different well come to him later
Use for local connections local sheet only
Global variable across all sheets – Shares properties with ”power” labels
Makes a pin visible on the hierachy block

## Slide 30: Hierarchical design – interfaces cont.
(like humans) Almost all pins have a type
Notes: Why is this good.
It looks nice
Our schematic design rule checker can see if we connect e.g output2output and kill our board

## Slide 31: Vector / Group bus
Vector bus
Group bus
Source: https://docs.kicad.org/master/en/eeschema/eeschema.html#buses

## Slide 32: Vector / Group bus
Source: https://docs.kicad.org/master/en/eeschema/eeschema.html#buses

## Slide 33: The Design rule checker <3
Our constraints
  In house fabrication
  JLC standard
DFM checker from kicad

## Slide 34: Life saving plugins
Interactive HTML-BOM
JLC export
https://octopart.com/

## Slide 35: Exercise: How to make s hield
You dont have to know everything, fortunately.
  We’ve done some work for you.
https://github.com/aausat/a6hwcommon/tree/main/CommonDEVBoard/shield_template_rev1
  kortlink.dk/2s42v